## Slide 1
This station allows for two way communication between caregiver and patient. The console has custom functions assigned to it, they are located at the bottom of the LCD Screen and are grouped in segments of four. The functions not displayed can be selected by toggling the left and right menu scroll keys.
Line Selector: Use these keys to select a line
Line Scroll Keys: Use these keys to scroll between stacked calls
Display: Displays current calls
Function Selector Keys: Use these keys to select the custom function above the key.
Menu Scroll Keys: Use these keys to scroll between custom functions. (in groups of 4)
Nurse Console:
Layer 1
Need RN
Night
Tones
Need CNA
Mute Tones
All Page
Vol +
Privacy
Vol -
Need RN/CNA: Sends a service request to the RN or LPN assigned to that room by lighting the corridor light above door and sending notification to wireless phone (if applicable.)
Mute Tones: Mutes call tones for 60 seconds, or until another call comes in.
Night Tones: Reduces call tone volume by half, with the exceptions of Staff Assist and Code Blue.
Layer 2
Vol+ / Vol- : Changes the volume of the patient station.
All Page: Pages all nurse call audio devices.
Privacy: HIPPA requirement. Mutes sound coming from pillow speaker. To set a room to Privacy, you first enter the Dial number then push the Privacy button (See reverse side for instructions.)
Layer 3
Delay Off
Delay On
Delay On
Delay Off
Delay On/Off: Delay should be on when wireless phones are in use and appropriately assigned. Turn delay off when needed. i.e. network down, phones down, assignments incomplete etc.
Delay Off:
When highlighted with border = NO delay. All calls ring immediately to console
Delay On:
When highlighted with border= DELAY PATIENT

## Slide 2: UNIT ED
To Dial a Patient Room From the Console:
1. Dial the room number on the keypad.
2. Lift the Handset.
3. Converse with the patient.
4. Hang up to end the call or you can push the cancel button on the console.
To Answer Calls at the Console:
When the console tones, lift the handset.
2. Converse with the patient.
3. Hang up to end the call or you can push the cancel button on the console.
To Set a Service at the Console:
To Dispatch Staff After Receiving Call From Patient
1. Answer patient call as described. Do not hang up.
2. Select need RN or Need PCA on the console and then hang up.
3. The corridor light above the room will flash the appropriate color for the service requested.
4. The service request will remain in the system until the caregiver hits the cancel button on the patient station.
To Dispatch Staff without a Patient Call
1. Pick up the handset and dial the room number. NOTE: This will open voice path to the room. The patient will be able to hear you.
2. Select need RN or Need PCT on the console and then hang up.
3. The corridor light above the room will flash the all appropriate color for the service requested.
4. The service request will remain active in the system until the caregiver hits cancel button on the patient station.
To Set Privacy or Monitor:
The privacy function will allow you to disable audio from the patient room out to the nurse station. This can be used if there is a need for a conversation to take place in the patient room and will ensure that no one can be listening in through the nurse call system.
To enable privacy enter the “dial number” of the room you want in privacy and press the “Privacy” button. You will see the room status change to “Privacy”.
To remove privacy, enter the “dial number” of the room and press “Privacy”. You will see the room status change again.
Room # | Dial #
ED 1 | 1001
ED 2 | 1002
ED 3 | 1003
ED 4 | 1004
ED 5 | 1005
ED 6 | 1006
ED 7 | 1007
ED 8 | 1008
ED 9 | 1009
ED 10 | 1010
ED 11 | 1011
ED 12 | 1012
ED 13 | 1013
ED 14 | 1014
ED 15 | 1015
ED 16 | 1016
Triage 1 | 10002
Triage 2 | 10001

## Slide 3
This station allows for two way communication between caregiver and patient. The console has custom functions assigned to it, they are located at the bottom of the LCD Screen and are grouped in segments of four. The functions not displayed can be selected by toggling the left and right menu scroll keys.
Line Selector: Use these keys to select a line
Line Scroll Keys: Use these keys to scroll between stacked calls
Display: Displays current calls
Function Selector Keys: Use these keys to select the custom function above the key.
Menu Scroll Keys: Use these keys to scroll between custom functions. (in groups of 4)
Nurse Console:
Layer 1
Need RN
Night
Tones
Need CNA
Mute Tones
All Page
Vol +
Privacy
Vol -
Need RN/CNA: Sends a service request to the RN or LPN assigned to that room by lighting the corridor light above door and sending notification to wireless phone (if applicable.)
Mute Tones: Mutes call tones for 60 seconds, or until another call comes in.
Night Tones: Reduces call tone volume by half, with the exceptions of Staff Assist and Code Blue.
Layer 2
Vol+ / Vol- : Changes the volume of the patient station.
All Page: Pages all nurse call audio devices.
Privacy: HIPPA requirement. Mutes sound coming from pillow speaker. To set a room to Privacy, you first enter the Dial number then push the Privacy button (See reverse side for instructions.)
Layer 3
Delay Off
Delay On
Delay On
Delay Off
Delay On/Off: Delay should be on when wireless phones are in use and appropriately assigned. Turn delay off when needed. i.e. network down, phones down, assignments incomplete etc.
Delay Off:
When highlighted with border = NO delay. All calls ring immediately to console
Delay On:
When highlighted with border= DELAY PATIENT

## Slide 4: UNIT Imaging
To Dial a Patient Room From the Console:
1. Dial the room number on the keypad.
2. Lift the Handset.
3. Converse with the patient.
4. Hang up to end the call or you can push the cancel button on the console.
To Answer Calls at the Console:
When the console tones, lift the handset.
2. Converse with the patient.
3. Hang up to end the call or you can push the cancel button on the console.
To Set a Service at the Console:
To Dispatch Staff After Receiving Call From Patient
1. Answer patient call as described. Do not hang up.
2. Select need RN or Need PCA on the console and then hang up.
3. The corridor light above the room will flash the appropriate color for the service requested.
4. The service request will remain in the system until the caregiver hits the cancel button on the patient station.
To Dispatch Staff without a Patient Call
1. Pick up the handset and dial the room number. NOTE: This will open voice path to the room. The patient will be able to hear you.
2. Select need RN or Need PCT on the console and then hang up.
3. The corridor light above the room will flash the all appropriate color for the service requested.
4. The service request will remain active in the system until the caregiver hits cancel button on the patient station.
To Set Privacy or Monitor:
The privacy function will allow you to disable audio from the patient room out to the nurse station. This can be used if there is a need for a conversation to take place in the patient room and will ensure that no one can be listening in through the nurse call system.
To enable privacy enter the “dial number” of the room you want in privacy and press the “Privacy” button. You will see the room status change to “Privacy”.
To remove privacy, enter the “dial number” of the room and press “Privacy”. You will see the room status change again.
Room # | Dial #
Ultrasound | 1108
MRI Scrn | 1304

## Slide 5
This station allows for two way communication between caregiver and patient. The console has custom functions assigned to it, they are located at the bottom of the LCD Screen and are grouped in segments of four. The functions not displayed can be selected by toggling the left and right menu scroll keys.
Line Selector: Use these keys to select a line
Line Scroll Keys: Use these keys to scroll between stacked calls
Display: Displays current calls
Function Selector Keys: Use these keys to select the custom function above the key.
Menu Scroll Keys: Use these keys to scroll between custom functions. (in groups of 4)
Nurse Console:
Layer 1
Need RN
Night
Tones
Need CNA
Mute Tones
All Page
Vol +
Privacy
Vol -
Need RN/CNA: Sends a service request to the RN or LPN assigned to that room by lighting the corridor light above door and sending notification to wireless phone (if applicable.)
Mute Tones: Mutes call tones for 60 seconds, or until another call comes in.
Night Tones: Reduces call tone volume by half, with the exceptions of Staff Assist and Code Blue.
Layer 2
Vol+ / Vol- : Changes the volume of the patient station.
All Page: Pages all nurse call audio devices.
Privacy: HIPPA requirement. Mutes sound coming from pillow speaker. To set a room to Privacy, you first enter the Dial number then push the Privacy button (See reverse side for instructions.)
Layer 3
Delay Off
Delay On
Delay On
Delay Off
Delay On/Off: Delay should be on when wireless phones are in use and appropriately assigned. Turn delay off when needed. i.e. network down, phones down, assignments incomplete etc.
Delay Off:
When highlighted with border = NO delay. All calls ring immediately to console
Delay On:
When highlighted with border= DELAY PATIENT

## Slide 6: UNIT 2 South
To Dial a Patient Room From the Console:
1. Dial the room number on the keypad.
2. Lift the Handset.
3. Converse with the patient.
4. Hang up to end the call or you can push the cancel button on the console.
To Answer Calls at the Console:
When the console tones, lift the handset.
2. Converse with the patient.
3. Hang up to end the call or you can push the cancel button on the console.
To Set a Service at the Console:
To Dispatch Staff After Receiving Call From Patient
1. Answer patient call as described. Do not hang up.
2. Select need RN or Need PCA on the console and then hang up.
3. The corridor light above the room will flash the appropriate color for the service requested.
4. The service request will remain in the system until the caregiver hits the cancel button on the patient station.
To Dispatch Staff without a Patient Call
1. Pick up the handset and dial the room number. NOTE: This will open voice path to the room. The patient will be able to hear you.
2. Select need RN or Need PCT on the console and then hang up.
3. The corridor light above the room will flash the all appropriate color for the service requested.
4. The service request will remain active in the system until the caregiver hits cancel button on the patient station.
To Set Privacy or Monitor:
The privacy function will allow you to disable audio from the patient room out to the nurse station. This can be used if there is a need for a conversation to take place in the patient room and will ensure that no one can be listening in through the nurse call system.
To enable privacy enter the “dial number” of the room you want in privacy and press the “Privacy” button. You will see the room status change to “Privacy”.
To remove privacy, enter the “dial number” of the room and press “Privacy”. You will see the room status change again.
Room # | Dial #
Pt Rm 2102 | 2102
Pt Rm 2106 | 2106
Pt Rm 2110 | 2110
Pt Rm 2114 | 2114
Pt Rm 2118 | 2118
Pt Rm 2122 | 2122
Pt Rm 2126 | 2126
Pt Rm 2130 | 2130
Pt Rm 2202 | 2202
Pt Rm 2204 | 2204
Pt Rm 2206 | 2206
Pt Rm 2208 | 2208
Pt Rm 2210 | 2210
Pt Rm 2212 | 2212
Pt Rm 2214 | 2214
Pt Rm 2216 | 2216
Pt Rm 2218 | 2218
Pt Rm 2220 | 2220
Pt Rm 2222 | 2222
Pt Rm 2224 | 2224
Pt Rm 2226 | 2226
Pt Rm 2228 | 2228
Pt Rm 2230 | 2230
Pt Rm 2232 | 2232

## Slide 7
This station allows for two way communication between caregiver and patient. The console has custom functions assigned to it, they are located at the bottom of the LCD Screen and are grouped in segments of four. The functions not displayed can be selected by toggling the left and right menu scroll keys.
Line Selector: Use these keys to select a line
Line Scroll Keys: Use these keys to scroll between stacked calls
Display: Displays current calls
Function Selector Keys: Use these keys to select the custom function above the key.
Menu Scroll Keys: Use these keys to scroll between custom functions. (in groups of 4)
Nurse Console:
Layer 1
Need RN
Night
Tones
Need CNA
Mute Tones
All Page
Vol +
Privacy
Vol -
Need RN/CNA: Sends a service request to the RN or LPN assigned to that room by lighting the corridor light above door and sending notification to wireless phone (if applicable.)
Mute Tones: Mutes call tones for 60 seconds, or until another call comes in.
Night Tones: Reduces call tone volume by half, with the exceptions of Staff Assist and Code Blue.
Layer 2
Vol+ / Vol- : Changes the volume of the patient station.
All Page: Pages all nurse call audio devices.
Privacy: HIPPA requirement. Mutes sound coming from pillow speaker. To set a room to Privacy, you first enter the Dial number then push the Privacy button (See reverse side for instructions.)
Layer 3
Delay Off
Delay On
Delay On
Delay Off
Delay On/Off: Delay should be on when wireless phones are in use and appropriately assigned. Turn delay off when needed. i.e. network down, phones down, assignments incomplete etc.
Delay Off:
When highlighted with border = NO delay. All calls ring immediately to console
Delay On:
When highlighted with border= DELAY PATIENT

## Slide 8: UNIT 3 North
To Dial a Patient Room From the Console:
1. Dial the room number on the keypad.
2. Lift the Handset.
3. Converse with the patient.
4. Hang up to end the call or you can push the cancel button on the console.
To Answer Calls at the Console:
When the console tones, lift the handset.
2. Converse with the patient.
3. Hang up to end the call or you can push the cancel button on the console.
To Set a Service at the Console:
To Dispatch Staff After Receiving Call From Patient
1. Answer patient call as described. Do not hang up.
2. Select need RN or Need PCA on the console and then hang up.
3. The corridor light above the room will flash the appropriate color for the service requested.
4. The service request will remain in the system until the caregiver hits the cancel button on the patient station.
To Dispatch Staff without a Patient Call
1. Pick up the handset and dial the room number. NOTE: This will open voice path to the room. The patient will be able to hear you.
2. Select need RN or Need PCT on the console and then hang up.
3. The corridor light above the room will flash the all appropriate color for the service requested.
4. The service request will remain active in the system until the caregiver hits cancel button on the patient station.
To Set Privacy or Monitor:
The privacy function will allow you to disable audio from the patient room out to the nurse station. This can be used if there is a need for a conversation to take place in the patient room and will ensure that no one can be listening in through the nurse call system.
To enable privacy enter the “dial number” of the room you want in privacy and press the “Privacy” button. You will see the room status change to “Privacy”.
To remove privacy, enter the “dial number” of the room and press “Privacy”. You will see the room status change again.
Room # | Dial #
Pt Rm 3502 | 3502
Pt Rm 3506 | 3506
Pt Rm 3510 | 3510
Pt Rm 3514 | 3514
Pt Rm 3518 | 3518
Pt Rm 3522 | 3522
Pt Rm 3526 | 3526
Pt Rm 3530 | 3530
Pt Rm 3402 | 3402
Pt Rm 3404 | 3404
Pt Rm 3406 | 3406
Pt Rm 3408 | 3408
Pt Rm 3410 | 3410
Pt Rm 3412 | 3412
Pt Rm 3414 | 3414
Pt Rm 3416 | 3416
Pt Rm 3418 | 3418
Pt Rm 3420 | 3420
Pt Rm 3422 | 3422
Pt Rm 3424 | 3424
Pt Rm 3426 | 3426
Pt Rm 3428 | 3428
Pt Rm 3430 | 3430
Pt Rm 3432 | 3432

## Slide 9
This station allows for two way communication between caregiver and patient. The console has custom functions assigned to it, they are located at the bottom of the LCD Screen and are grouped in segments of four. The functions not displayed can be selected by toggling the left and right menu scroll keys.
Line Selector: Use these keys to select a line
Line Scroll Keys: Use these keys to scroll between stacked calls
Display: Displays current calls
Function Selector Keys: Use these keys to select the custom function above the key.
Menu Scroll Keys: Use these keys to scroll between custom functions. (in groups of 4)
Nurse Console:
Layer 1
Need RN
Night
Tones
Need CNA
Mute Tones
All Page
Vol +
Privacy
Vol -
Need RN/CNA: Sends a service request to the RN or LPN assigned to that room by lighting the corridor light above door and sending notification to wireless phone (if applicable.)
Mute Tones: Mutes call tones for 60 seconds, or until another call comes in.
Night Tones: Reduces call tone volume by half, with the exceptions of Staff Assist and Code Blue.
Layer 2
Vol+ / Vol- : Changes the volume of the patient station.
All Page: Pages all nurse call audio devices.
Privacy: HIPPA requirement. Mutes sound coming from pillow speaker. To set a room to Privacy, you first enter the Dial number then push the Privacy button (See reverse side for instructions.)
Layer 3
Delay Off
Delay On
Delay On
Delay Off
Delay On/Off: Delay should be on when wireless phones are in use and appropriately assigned. Turn delay off when needed. i.e. network down, phones down, assignments incomplete etc.
Delay Off:
When highlighted with border = NO delay. All calls ring immediately to console
Delay On:
When highlighted with border= DELAY PATIENT

## Slide 10: UNIT 3 South
To Dial a Patient Room From the Console:
1. Dial the room number on the keypad.
2. Lift the Handset.
3. Converse with the patient.
4. Hang up to end the call or you can push the cancel button on the console.
To Answer Calls at the Console:
When the console tones, lift the handset.
2. Converse with the patient.
3. Hang up to end the call or you can push the cancel button on the console.
To Set a Service at the Console:
To Dispatch Staff After Receiving Call From Patient
1. Answer patient call as described. Do not hang up.
2. Select need RN or Need PCA on the console and then hang up.
3. The corridor light above the room will flash the appropriate color for the service requested.
4. The service request will remain in the system until the caregiver hits the cancel button on the patient station.
To Dispatch Staff without a Patient Call
1. Pick up the handset and dial the room number. NOTE: This will open voice path to the room. The patient will be able to hear you.
2. Select need RN or Need PCT on the console and then hang up.
3. The corridor light above the room will flash the all appropriate color for the service requested.
4. The service request will remain active in the system until the caregiver hits cancel button on the patient station.
To Set Privacy or Monitor:
The privacy function will allow you to disable audio from the patient room out to the nurse station. This can be used if there is a need for a conversation to take place in the patient room and will ensure that no one can be listening in through the nurse call system.
To enable privacy enter the “dial number” of the room you want in privacy and press the “Privacy” button. You will see the room status change to “Privacy”.
To remove privacy, enter the “dial number” of the room and press “Privacy”. You will see the room status change again.
Room # | Dial #
Pt Rm 3102 | 3102
Pt Rm 3106 | 3106
Pt Rm 3110 | 3110
Pt Rm 3114 | 3114
Pt Rm 3118 | 3118
Pt Rm 3122 | 3122
Pt Rm 3126 | 3126
Pt Rm 3130 | 3130
Pt Rm 3232 | 3232
Pt Rm 3230 | 3230
Pt Rm 3228 | 3228
Pt Rm 3226 | 3226
Pt Rm 3224 | 3224
Pt Rm 3222 | 3222
Pt Rm 3220 | 3220
Pt Rm 3218 | 3218
Pt Rm 3216 | 3216
Pt Rm 3214 | 3214
Pt Rm 3210 | 3210
Pt Rm 3208 | 3208
Pt Rm 3206 | 3206
Pt Rm 3204 | 3204
Pt Rm 3202 | 3202

## Slide 11
This station allows for two way communication between caregiver and patient. The console has custom functions assigned to it, they are located at the bottom of the LCD Screen and are grouped in segments of four. The functions not displayed can be selected by toggling the left and right menu scroll keys.
Line Selector: Use these keys to select a line
Line Scroll Keys: Use these keys to scroll between stacked calls
Display: Displays current calls
Function Selector Keys: Use these keys to select the custom function above the key.
Menu Scroll Keys: Use these keys to scroll between custom functions. (in groups of 4)
Nurse Console:
Layer 1
Need RN
Night
Tones
Need CNA
Mute Tones
All Page
Vol +
Privacy
Vol -
Need RN/CNA: Sends a service request to the RN or LPN assigned to that room by lighting the corridor light above door and sending notification to wireless phone (if applicable.)
Mute Tones: Mutes call tones for 60 seconds, or until another call comes in.
Night Tones: Reduces call tone volume by half, with the exceptions of Staff Assist and Code Blue.
Layer 2
Vol+ / Vol- : Changes the volume of the patient station.
All Page: Pages all nurse call audio devices.
Privacy: HIPPA requirement. Mutes sound coming from pillow speaker. To set a room to Privacy, you first enter the Dial number then push the Privacy button (See reverse side for instructions.)
Layer 3
Delay Off
Delay On
Delay On
Delay Off
Delay On/Off: Delay should be on when wireless phones are in use and appropriately assigned. Turn delay off when needed. i.e. network down, phones down, assignments incomplete etc.
Delay Off:
When highlighted with border = NO delay. All calls ring immediately to console
Delay On:
When highlighted with border= DELAY PATIENT

## Slide 12: UNIT 4PRE
To Dial a Patient Room From the Console:
1. Dial the room number on the keypad.
2. Lift the Handset.
3. Converse with the patient.
4. Hang up to end the call or you can push the cancel button on the console.
To Answer Calls at the Console:
When the console tones, lift the handset.
2. Converse with the patient.
3. Hang up to end the call or you can push the cancel button on the console.
To Set a Service at the Console:
To Dispatch Staff After Receiving Call From Patient
1. Answer patient call as described. Do not hang up.
2. Select need RN or Need PCA on the console and then hang up.
3. The corridor light above the room will flash the appropriate color for the service requested.
4. The service request will remain in the system until the caregiver hits the cancel button on the patient station.
To Dispatch Staff without a Patient Call
1. Pick up the handset and dial the room number. NOTE: This will open voice path to the room. The patient will be able to hear you.
2. Select need RN or Need PCT on the console and then hang up.
3. The corridor light above the room will flash the all appropriate color for the service requested.
4. The service request will remain active in the system until the caregiver hits cancel button on the patient station.
To Set Privacy or Monitor:
The privacy function will allow you to disable audio from the patient room out to the nurse station. This can be used if there is a need for a conversation to take place in the patient room and will ensure that no one can be listening in through the nurse call system.
To enable privacy enter the “dial number” of the room you want in privacy and press the “Privacy” button. You will see the room status change to “Privacy”.
To remove privacy, enter the “dial number” of the room and press “Privacy”. You will see the room status change again.
Room # | Dial #
Preop 1 | 4001
Preop 2 | 4002
Preop 3 | 4003
Preop 4 | 4004
Preop 5 | 4005
Preop 6 | 4006
Preop 7 | 4007
Preop 8 | 4008
Preop 9 | 4009
Preop 10 | 4010
Preop 11 | 4011
Preop 12 | 4012
Preop 13 | 4013
Preop 14 | 4014
Preop 15 | 4015

## Slide 13
This station allows for two way communication between caregiver and patient. The console has custom functions assigned to it, they are located at the bottom of the LCD Screen and are grouped in segments of four. The functions not displayed can be selected by toggling the left and right menu scroll keys.
Line Selector: Use these keys to select a line
Line Scroll Keys: Use these keys to scroll between stacked calls
Display: Displays current calls
Function Selector Keys: Use these keys to select the custom function above the key.
Menu Scroll Keys: Use these keys to scroll between custom functions. (in groups of 4)
Nurse Console:
Layer 1
Need RN
Night
Tones
Need CNA
Mute Tones
All Page
Vol +
Privacy
Vol -
Need RN/CNA: Sends a service request to the RN or LPN assigned to that room by lighting the corridor light above door and sending notification to wireless phone (if applicable.)
Mute Tones: Mutes call tones for 60 seconds, or until another call comes in.
Night Tones: Reduces call tone volume by half, with the exceptions of Staff Assist and Code Blue.
Layer 2
Vol+ / Vol- : Changes the volume of the patient station.
All Page: Pages all nurse call audio devices.
Privacy: HIPPA requirement. Mutes sound coming from pillow speaker. To set a room to Privacy, you first enter the Dial number then push the Privacy button (See reverse side for instructions.)
Layer 3
Delay Off
Delay On
Delay On
Delay Off
Delay On/Off: Delay should be on when wireless phones are in use and appropriately assigned. Turn delay off when needed. i.e. network down, phones down, assignments incomplete etc.
Delay Off:
When highlighted with border = NO delay. All calls ring immediately to console
Delay On:
When highlighted with border= DELAY PATIENT

## Slide 14: UNIT 4PAC
To Dial a Patient Room From the Console:
1. Dial the room number on the keypad.
2. Lift the Handset.
3. Converse with the patient.
4. Hang up to end the call or you can push the cancel button on the console.
To Answer Calls at the Console:
When the console tones, lift the handset.
2. Converse with the patient.
3. Hang up to end the call or you can push the cancel button on the console.
To Set a Service at the Console:
To Dispatch Staff After Receiving Call From Patient
1. Answer patient call as described. Do not hang up.
2. Select need RN or Need PCA on the console and then hang up.
3. The corridor light above the room will flash the appropriate color for the service requested.
4. The service request will remain in the system until the caregiver hits the cancel button on the patient station.
To Dispatch Staff without a Patient Call
1. Pick up the handset and dial the room number. NOTE: This will open voice path to the room. The patient will be able to hear you.
2. Select need RN or Need PCT on the console and then hang up.
3. The corridor light above the room will flash the all appropriate color for the service requested.
4. The service request will remain active in the system until the caregiver hits cancel button on the patient station.
To Set Privacy or Monitor:
The privacy function will allow you to disable audio from the patient room out to the nurse station. This can be used if there is a need for a conversation to take place in the patient room and will ensure that no one can be listening in through the nurse call system.
To enable privacy enter the “dial number” of the room you want in privacy and press the “Privacy” button. You will see the room status change to “Privacy”.
To remove privacy, enter the “dial number” of the room and press “Privacy”. You will see the room status change again.
Room # | Dial #
PACU 16 | 4016
PACU 17 | 4017
PACU 18 | 4018
PACU 19 | 4019
PACU 20 | 4020
PACU 21 | 4021
PACU 22 | 4022
PACU 23 | 4023
PACU 24 | 4024
PACU 25 | 4025
PACU 26 | 4026
PACU 27 | 4027
PACU 28 | 4028
PACU 29 | 4029
PACU 30 | 4030