## Slide 1
{Distributor Logo}
St. Francis - InterQuest
Notes: {Everything in brackets { … } is to be set up BEFORE going into the meeting.

## Slide 2: Device Overview
Nurse Console
Dome/Zone
Light
Enhanced Patient
Station
Pillow Speaker
Pull Cord
Feature Bed Interface
2-Jack
2-Button
Duty Station
Call Cord
Staff Assist
Device

## Slide 3: Patient Call
Corridor Light Display:
Flashing white light in segment 1 above the patient’s door.
Tone Type:
Slow Ding
Console will ring
after 1 minute(when delay
button is activated).
30 secs
NC
30 secs
To Cancel Call:
Answer call
Enter room with badge
Press cancel button
Call Stop 1
CNA
RN
Call Stop 2

## Slide 4
Pain Call
Tone Type:
Slow Ding
Corridor Light Display:
Flashing white and green lights in segments 1 and 2 above the patient’s door.
30 secs
NC
30 secs
Console will ring
after 1 minute(when delay
button is activated).
To Cancel Call:
Answer call
Enter room with badge
Press cancel button
Call Stop 1
CNA
RN
Call Stop 2

## Slide 5
Water Call
Tone Type:
Slow Ding
Corridor Light Display:
Flashing white and orange lights in segments 1 and 2 above the patient’s door.
30 secs
NC
30 secs
Console will ring
after 1 minute(when delay
button is activated).
To Cancel Call:
Answer call
Enter room with badge
Press cancel button
Call Stop 1
CNA
RN
Call Stop 2

## Slide 6
Tone Type:
Slow Ding
Corridor Light Display:
Flashing white and red and orange lights in segments 1 and 2 and 3 above the patient’s door.
To Cancel Call:
Answer call
Enter room with badge
Press cancel button
Toilet Assist Call
30 secs
NC
30 secs
Console will ring
after 1 minute(when delay
button is activated).
Call Stop 1
CNA
RN
Call Stop 2

## Slide 7
Tone Type:
Fast Ding
Corridor Light Display:
Flashing Red lights in segments 3 and 4 above the patient’s door.
Console will ring
immediately.
To Cancel Call:
Press cancel button
Toilet/ Shower Emergency
Urgent Call Option: (This is an option to receive all urgent calls from all rooms.)
(Uncheck box to receive urgent calls from your rooms only.)

## Slide 8
Tone Type:
Fast Ding
Corridor Light Display:
Cascading yellow lights in all 4 segments above the patient’s door.
Console will ring
immediately.
To Cancel Call:
Press cancel button
Bed Exit
Urgent Call Option: (This is an option to receive all urgent calls from all rooms.)
(Uncheck box to receive urgent calls from your rooms only.)

## Slide 9
Tone Type:
Fast Ding
Corridor Light Display:
Cascading yellow lights in all 4 segments above the patient’s door.
Console will ring
immediately.
To Cancel Call:
Press cancel button
Chair Alarm
Urgent Call Option: (This is an option to receive all urgent calls from all rooms.)
(Uncheck box to receive urgent calls from your rooms only.)

## Slide 10
Console will ring
immediately.
To Cancel Call:
Press cancel button
Cord Out / Plug Out / Bed Out
Tone Type:
Medium Ding
Corridor Light Display:
Flashing white lights in segments 1 and 2 above the patient’s door.

## Slide 11
Staff Assist
Urgent Call Option: (This is an option to receive all urgent calls from all rooms.)
(Uncheck box to receive urgent calls from your rooms only.)
To Cancel Call:
Press cancel button
Tone Type:
Fast Ding
Corridor Light Display:
Cascading red lights in all 4 segments above the patient’s door.
Console will ring immediately.
Local console(s)
Annunciation at Duty Stations on unit.

## Slide 12
Urgent Call Option: (This is an option to receive all urgent calls from all rooms.)
(Uncheck box to receive urgent calls from your rooms only.)
To Cancel Call:
Press cancel button
Tone Type:
Warble
Corridor Light Display:
Cascading blue lights in all 4 segments above the patient’s door.
Console will ring immediately.
Local console(s)
PBX
Annunciation at Duty Stations on unit.
Code Blue

## Slide 13: RN Present
Tone Type: No tone.
Corridor Light Display:
Solid green light in segment 2 above the patient’s door.
CNA Present
Tone Type: No tone.
Corridor Light Display:
Solid Orange light in segment 3 above the patient’s door.
PT/OT Present
Tone Type: No tone.
Corridor Light Display:
Solid White light in segment 3 above the patient’s door.
Tone Type: No tone.
Corridor Light Display:
Solid Blue light in segment 3 above the patient’s door.
MD/LIP Present

## Slide 14: Rounds Workflow:
1:01 hours.
1:00 hour
Light Only
2,3 pink solid
3 pink solid
Light Only
Button press
initiates timer
To Cancel
Toggle on/off NC