## Slide 1: Enterprise Device Training Guide ED

## Slide 2
ENHANCED PATIENT STATION
Patient
Water
Flashing Light
Slow Ding
Flashing Lights
Slow Ding
Need Toilet
In Pain
Flashing Lights
Slow Ding
Flashing Lights
Slow Ding
PILLOW SPEAKER
SFI: ENTERPRISE DEVICES – ED
Overhead
Light Controls
TV Controls
Cancel Button
Auxiliary Jack
For a specialty call cord (touch pad, squeeze ball, etc.) It will initiate a patient call
Code Blue
Staff will press this button to initiate an urgent alert
Fast Cascade Lights
Warble
Staff Assist Button
Staff will press this button to initiate an urgent alert
Flashing Lights
Fast Ding
Cord Out / Plug out
Occurs when the Pillow Speaker or Call Cord has been removed
Flashing Light
Medium Ding
5 sec grace
PILLOW SPEAKER
IF STAFF WANT TO REMOVE ANY CORD FROM THE PATIENT STATION AND NOT INITIATE AN ALARM.
UNPLUG THE DEVICE
PRESS THE CANCEL BUTTON WITHIN 5 SECONDS

## Slide 3
SFI: ENTERPRISE DEVICES
ED
6/8/2023
PATIENT BATHROOM PULL CORD
Toilet
Console – Immediately
Flashing Lights
Fast Ding
Cancel Button
DUTY STATION
Cancel Button
Call Button – Staff can place a call to the Master Console
Dome Lights –
Mimics highest priority active call light
Cancel Button
Chair Alarm
Console – Immediately
Flashing Light
Fast Ding
Chair Alarm
Console – Immediately
Flashing Light
Medium Ding
5 sec grace
IF STAFF WANT TO REMOVE ANY CORD FROM THE PATIENT STATION AND NOT INITIATE AN ALARM.
UNPLUG THE DEVICE
PRESS THE CANCEL BUTTON WITHIN 5 SECONDS
Flashing Lights
Fast Ding
2-JACK AUXILIARY JACK STATION
Cord Out

## Slide 4: Enterprise Device Training Guide Imaging

## Slide 5
ENHANCED PATIENT STATION
Patient
Water
Flashing Light
Slow Ding
Flashing Lights
Slow Ding
Need Toilet
In Pain
Flashing Lights
Slow Ding
Flashing Lights
Slow Ding
PILLOW SPEAKER
SFI: ENTERPRISE DEVICES – Imaging
Overhead
Light Controls
TV Controls
Cancel Button
Auxiliary Jack
For a specialty call cord (touch pad, squeeze ball, etc.) It will initiate a patient call
Code Blue
Staff will press this button to initiate an urgent alert
Fast Cascade Lights
Warble
Staff Assist Button
Staff will press this button to initiate an urgent alert
Flashing Lights
Fast Ding
Cord Out / Plug out
Occurs when the Pillow Speaker or Call Cord has been removed
Flashing Light
Medium Ding
5 sec grace
PILLOW SPEAKER
IF STAFF WANT TO REMOVE ANY CORD FROM THE PATIENT STATION AND NOT INITIATE AN ALARM.
UNPLUG THE DEVICE
PRESS THE CANCEL BUTTON WITHIN 5 SECONDS

## Slide 6
SFI: ENTERPRISE DEVICES
IMAGING
6/8/2023
PATIENT BATHROOM PULL CORD
Toilet
Console – Immediately
Flashing Lights
Fast Ding
Cancel Button
Code Blue
Staff will press this button to initiate an urgent alert
Fast Cascading Lights
Warble
Cancel Button
Rapid Response Button
Staff will press this button to initiate an urgent alert
Flashing Lights
Fast Ding
DUAL PUSH BUTTON
STATION
DUTY STATION
Cancel Button
Call Button – Staff can place a call to the Master Console
Dome Lights –
Mimics highest priority active call light

## Slide 7: Enterprise Device Training Guide 2 South

## Slide 8
ENHANCED PATIENT STATION
Patient
Water
Flashing Light
Slow Ding
Flashing Lights
Slow Ding
Need Toilet
In Pain
Flashing Lights
Slow Ding
Flashing Lights
Slow Ding
PILLOW SPEAKER
SFI: ENTERPRISE DEVICES – 2 South
Overhead
Light Controls
TV Controls
Cancel Button
Auxiliary Jack
For a specialty call cord (touch pad, squeeze ball, etc.) It will initiate a patient call
Code Blue
Staff will press this button to initiate an urgent alert
Fast Cascade Lights
Warble
Staff Assist Button
Staff will press this button to initiate an urgent alert
Flashing Lights
Fast Ding
Cord Out / Plug out
Occurs when the Pillow Speaker or Call Cord has been removed
Flashing Light
Medium Ding
5 sec grace
PILLOW SPEAKER
IF STAFF WANT TO REMOVE ANY CORD FROM THE PATIENT STATION AND NOT INITIATE AN ALARM.
UNPLUG THE DEVICE
PRESS THE CANCEL BUTTON WITHIN 5 SECONDS

## Slide 9
2-JACK AUXILIARY JACK STATION
Cancel Button
Chair Alarm
Console – Immediately
Flashing Light
Fast Ding
Chair Alarm
Console – Immediately
Cord Out
Occurs when the Call Cord has been removed
SFI: ENTERPRISE DEVICES – 2 South
Flashing Light
Medium Ding
5 sec grace
IF STAFF WANT TO REMOVE ANY CORD FROM THE PATIENT STATION AND NOT INITIATE AN ALARM.
UNPLUG THE DEVICE
PRESS THE CANCEL BUTTON WITHIN 5 SECONDS
Flashing Lights
Fast Ding
FEATURE BED MODULE
Bed Out
Occurs when the Feature Bed plug has been removed
Console – After 5 seconds
Flashing Light
Medium Ding
5 sec grace
IF STAFF WANT TO REMOVE ANY CORD FROM THE PATIENT STATION AND NOT INITIATE AN ALARM.
UNPLUG THE DEVICE
PRESS THE CANCEL BUTTON WITHIN 5 SECONDS
Dummy Plug – Insert the dummy plug to protect the bed connection
Bed Exit
Occurs when the alarm on the bed is initiated
Console – Immediately
Clear the alarm on the bed then use the cancel button on the Patient Station to clear the alert
Flashing Lights
Fast Ding

## Slide 10
SFI: ENTERPRISE DEVICES – 2 South
6/8/2023
PATIENT BATHROOM PULL CORD
Toilet
Console – Immediately
Flashing Lights
Medium Ding
Cancel Button
DUTY STATION
Cancel Button
Call Button – Staff can place a call to the Master Console
Dome Lights –
Mimics highest priority active call light

## Slide 11: Enterprise Device Training Guide 3 South

## Slide 12
ENHANCED PATIENT STATION
Patient
Water
Flashing Light
Slow Ding
Flashing Lights
Slow Ding
Need Toilet
In Pain
Flashing Lights
Slow Ding
Flashing Lights
Slow Ding
PILLOW SPEAKER
SFI: ENTERPRISE DEVICES – 3 South
Overhead
Light Controls
TV Controls
Cancel Button
Auxiliary Jack
For a specialty call cord (touch pad, squeeze ball, etc.) It will initiate a patient call
Code Blue
Staff will press this button to initiate an urgent alert
Fast Cascade Lights
Warble
Staff Assist Button
Staff will press this button to initiate an urgent alert
Flashing Lights
Fast Ding
Cord Out / Plug out
Occurs when the Pillow Speaker or Call Cord has been removed
Flashing Light
Medium Ding
5 sec grace
PILLOW SPEAKER
IF STAFF WANT TO REMOVE ANY CORD FROM THE PATIENT STATION AND NOT INITIATE AN ALARM.
UNPLUG THE DEVICE
PRESS THE CANCEL BUTTON WITHIN 5 SECONDS

## Slide 13
2-JACK AUXILIARY JACK STATION
Cancel Button
Chair Alarm
Console – Immediately
Flashing Light
Fast Ding
Chair Alarm
Console – Immediately
Cord Out
Occurs when the Call Cord has been removed
SFI: ENTERPRISE DEVICES – 3 South
Flashing Light
Medium Ding
5 sec grace
IF STAFF WANT TO REMOVE ANY CORD FROM THE PATIENT STATION AND NOT INITIATE AN ALARM.
UNPLUG THE DEVICE
PRESS THE CANCEL BUTTON WITHIN 5 SECONDS
Flashing Lights
Fast Ding
FEATURE BED MODULE
Bed Out
Occurs when the Feature Bed plug has been removed
Console – After 5 seconds
Flashing Light
Medium Ding
5 sec grace
IF STAFF WANT TO REMOVE ANY CORD FROM THE PATIENT STATION AND NOT INITIATE AN ALARM.
UNPLUG THE DEVICE
PRESS THE CANCEL BUTTON WITHIN 5 SECONDS
Dummy Plug – Insert the dummy plug to protect the bed connection
Bed Exit
Occurs when the alarm on the bed is initiated
Console – Immediately
Clear the alarm on the bed then use the cancel button on the Patient Station to clear the alert
Flashing Lights
Fast Ding

## Slide 14
SFI: ENTERPRISE DEVICES – 3 South
6/8/2023
PATIENT BATHROOM PULL CORD
Toilet
Console – Immediately
Flashing Lights
Medium Ding
Cancel Button
DUTY STATION
Cancel Button
Call Button – Staff can place a call to the Master Console
Dome Lights –
Mimics highest priority active call light
Cancel Button
Staff Assist Button
Staff will press this button to initiate an urgent alert
Fast Cascading Lights
Fast Ding
STAFF ASSIST BUTTON
STATION

## Slide 15: Enterprise Device Training Guide 3 North

## Slide 16
ENHANCED PATIENT STATION
Patient
Water
Flashing Light
Slow Ding
Flashing Lights
Slow Ding
Need Toilet
In Pain
Flashing Lights
Slow Ding
Flashing Lights
Slow Ding
PILLOW SPEAKER
SFI: ENTERPRISE DEVICES – 3 North
Overhead
Light Controls
TV Controls
Cancel Button
Auxiliary Jack
For a specialty call cord (touch pad, squeeze ball, etc.) It will initiate a patient call
Code Blue
Staff will press this button to initiate an urgent alert
Fast Cascade Lights
Warble
Staff Assist Button
Staff will press this button to initiate an urgent alert
Flashing Lights
Fast Ding
Cord Out / Plug out
Occurs when the Pillow Speaker or Call Cord has been removed
Flashing Light
Medium Ding
5 sec grace
PILLOW SPEAKER
IF STAFF WANT TO REMOVE ANY CORD FROM THE PATIENT STATION AND NOT INITIATE AN ALARM.
UNPLUG THE DEVICE
PRESS THE CANCEL BUTTON WITHIN 5 SECONDS

## Slide 17
2-JACK AUXILIARY JACK STATION
Cancel Button
Chair Alarm
Console – Immediately
Flashing Light
Fast Ding
Chair Alarm
Console – Immediately
Cord Out
Occurs when the Call Cord has been removed
SFI: ENTERPRISE DEVICES – 3 North
Flashing Light
Medium Ding
5 sec grace
IF STAFF WANT TO REMOVE ANY CORD FROM THE PATIENT STATION AND NOT INITIATE AN ALARM.
UNPLUG THE DEVICE
PRESS THE CANCEL BUTTON WITHIN 5 SECONDS
Flashing Lights
Fast Ding
FEATURE BED MODULE
Bed Out
Occurs when the Feature Bed plug has been removed
Console – After 5 seconds
Flashing Light
Medium Ding
5 sec grace
IF STAFF WANT TO REMOVE ANY CORD FROM THE PATIENT STATION AND NOT INITIATE AN ALARM.
UNPLUG THE DEVICE
PRESS THE CANCEL BUTTON WITHIN 5 SECONDS
Dummy Plug – Insert the dummy plug to protect the bed connection
Bed Exit
Occurs when the alarm on the bed is initiated
Console – Immediately
Clear the alarm on the bed then use the cancel button on the Patient Station to clear the alert
Flashing Lights
Fast Ding

## Slide 18
SFI: ENTERPRISE DEVICES – 3 North
6/8/2023
PATIENT BATHROOM PULL CORD
Toilet
Console – Immediately
Flashing Lights
Medium Ding
Cancel Button
DUTY STATION
Cancel Button
Call Button – Staff can place a call to the Master Console
Dome Lights –
Mimics highest priority active call light
Cancel Button
Staff Assist Button
Staff will press this button to initiate an urgent alert
Fast Cascading Lights
Fast Ding
STAFF ASSIST BUTTON
STATION

## Slide 19: Enterprise Device Training Guide OR

## Slide 20
SFI: ENTERPRISE DEVICES – OR
6/8/2023
Code Blue
Staff will press this button to initiate an urgent alert
Fast Cascading Lights
Warble
Cancel Button
Staff Assist Button
Staff will press this button to initiate an urgent alert
Fast Cascading Lights
Fast Ding
DUAL PUSH BUTTON
STATION
DUTY STATION
Cancel Button
Call Button – Staff can place a call to the Master Console
Dome Lights –
Mimics highest priority active call light

## Slide 21: Enterprise Device Training Guide 4PRE

## Slide 22
ENHANCED PATIENT STATION
Patient
Flashing Light
Slow Ding
CALL CORD
SFI: ENTERPRISE DEVICES – 4PRE
Cancel Button
Auxiliary Jack
For a specialty call cord (touch pad, squeeze ball, etc.) It will initiate a patient call
Code Blue
Staff will press this button to initiate an urgent alert
Fast Cascade Lights
Warble
Rapid Response Button
Staff will press this button to initiate an urgent alert
Flashing Lights
Fast Ding
Cord Out / Plug out
Occurs when the Pillow Speaker or Call Cord has been removed
Flashing Light
Medium Ding
5 sec grace
CALL CORD
IF STAFF WANT TO REMOVE ANY CORD FROM THE PATIENT STATION AND NOT INITIATE AN ALARM.
UNPLUG THE DEVICE
PRESS THE CANCEL BUTTON WITHIN 5 SECONDS

## Slide 23
SFI: ENTERPRISE DEVICES – 4PRE
6/8/2023
PATIENT BATHROOM PULL CORD
Toilet
Console – Immediately
Flashing Lights
Medium Ding
Cancel Button
DUTY STATION
Cancel Button
Call Button – Staff can place a call to the Master Console
Dome Lights –
Mimics highest priority active call light

## Slide 24: Enterprise Device Training Guide 4PAC

## Slide 25
ENHANCED PATIENT STATION
Patient
Flashing Light
Slow Ding
CALL CORD
SFI: ENTERPRISE DEVICES – 4PAC
Cancel Button
Auxiliary Jack
For a specialty call cord (touch pad, squeeze ball, etc.) It will initiate a patient call
Code Blue
Staff will press this button to initiate an urgent alert
Fast Cascade Lights
Warble
Rapid Response Button
Staff will press this button to initiate an urgent alert
Flashing Lights
Fast Ding
Cord Out / Plug out
Occurs when the Pillow Speaker or Call Cord has been removed
Flashing Light
Medium Ding
5 sec grace
CALL CORD
IF STAFF WANT TO REMOVE ANY CORD FROM THE PATIENT STATION AND NOT INITIATE AN ALARM.
UNPLUG THE DEVICE
PRESS THE CANCEL BUTTON WITHIN 5 SECONDS

## Slide 26
SFI: ENTERPRISE DEVICES – 4PAC
6/8/2023
PATIENT BATHROOM PULL CORD
Toilet
Console – Immediately
Flashing Lights
Medium Ding
Cancel Button
DUTY STATION
Cancel Button
Call Button – Staff can place a call to the Master Console
Dome Lights –
Mimics highest priority active call light